## Slide 1: Liz Brierley
        Liz is an experienced leader with demonstrated capability in building effective teams to manage high risk assets in a regulated environment across multiple State jurisdictions. She has an extensive knowledge of pipelines, gas networks and related energy systems that has been developed through more than 20 years working for gas network and pipeline operators, with more than fifteen years’ experience in leadership roles.
        A proven ability to work collaboratively to influence change in organisations, standards and legislation. Liz has been actively involved in the development of Australian Standards for pipelines for more than 10 years, recently appointed chair of the ME-38.3 Sub-Committee.
        One of the first Chartered Professional (Oil and Gas Pipeline) Engineers in Australia, she follows a passion to promote high quality engineering education and professional development as a member of the National Engineering Registration Board Assessment Panel for Oil and Gas Pipeline Engineers.
Head of Asset Management
SEA Gas

## Slide 2: AS 2885.3 Seminar
Section 7 – Pipeline Corridor Management
Presented By – Liz Brierley

## Slide 3: Section 7 – Pipeline Corridor Management
Basis of Section
  The control of threats associated with first and third party activity or natural events both on or adjacent to the pipeline corridor that have the potential to impact pipeline integrity.
Key Concepts
  Managing external interference in a pipeline corridor
  Corridor surveillance for natural hazards
  Vegetation management
  Controlling external loads
  Managing the threat of vibration and blasting
  Management of land use change within the measurement length

## Slide 4: Objectives of 2022 Update
Clarify the scope
Improve structure
Align with AS2885.6 and the SMS process.
Address non-external interference threats
Other Minor Changes
Emergency Services Liaison has moved to Section 11
Added guidance remote intrusion monitoring

## Slide 5: Pipeline corridor management vs External interference management
  Pipeline corridor management is broader than just External Interference:
  External Interference is the removal of, or penetration of, the protective ground cover and potential contact with the pipe
    Other activities occur on or near the pipeline corridor which may impact the operation of the pipeline
  Procedural controls apply specifically to external interference threats
    But may also reduce the risk associated with other threats
Section 7 details the minimum requirements for pipeline corridor management to control and monitor activities near pipeline systems, including, but not limited to external interference and procedural controls.

## Slide 6: Interface with AS2885.6
AS2885.3
  Procedures for identification of new EI threats
  Minimum requirements for EI procedural controls
  Requirement to review and ensure EI threat controls are effective
AS 2885.6
  EI threat identification and controls
  Risk assessment and risk management for EI threats
  Determination of appropriate controls for EI threats
  Triggers for SMS review

## Slide 7: Section 7 - 2022 Structure
  7.1 Basis of Section
  7.2 External interference management
  7.3 Procedural controls
    7.3.1 General
    7.3.2 Liaison (Landowner and occupier liaison/Planning and development liaison/Third party liaison)
    7.3.3 One-call services
    7.3.4 Pipeline marking
    7.3.5 Agreements with other entities
    7.3.6 Pipeline system patrol program
    7.3.7 Remote Intrusion monitoring
  7.4 Corridor surveillance
  7.5 Controlling activities near pipeline systems
    7.5.1 Procedures for controlling third party activities
    7.5.2 Licensee’s own activities
    7.5.3 Stress and strain
    7.5.4 Placement of material on or near the pipeline system
    7.5.5 Vibration in the vicinity of the pipeline system
    7.5.6 Vegetation on or near the pipeline system
    7.5.7 Pipeline corridor access
    7.5.8 Temporary pipelines installed above ground or with reduced depth of cover
Section 7 - 2012 Structure

## Slide 8: Patrols
Minimum frequency is annual.
Method and frequency must be designed to identify:
  Variations in surface conditions
  Indications of leaks
  Excessive growth of vegetation
  Impediments to site access.
  Changes to landform resulting in axial or bending strain.
Must have a clearly defined scope and observations must be recorded.
Corridor Surveillance
Frequency determined by SMS documented in PIMP
Seeks to identify:
  Construction Activity
  Land use change
  Effectiveness of marker signs
  Security of sites
Records must be maintained for 10 yrs and inform SMS Review

## Slide 9: 7.5.1 - Procedures For Controlling Third Party Works
Minimum notice period for intended activities near a pipeline system
Requirements for pipeline operator site supervision
Requirements for third party procedures
Restrictions on the use of mechanical equipment
Requirements for and acceptable methods of pipeline location
Minimum separation distances to above ground permanent structures
Requirements for installing buried services that cross or are parallel to the pipeline.
Pipeline minimum depth of cover
Pipeline stress and strain limits
Backfill and compaction requirements
Notification requirements if a pipeline is damaged
Vibration limits
Restrictions on placement of spoil in a pipeline corridor
Requirements for work adjacent to a pipeline corridor
Requirements for directionally drilling across a pipeline
Requirements for ground disturbing activities deeper than 300mm
Work procedures shall be documented in the PMS and shall include:

## Slide 10: Additional requirements and guidance on corridor management for non-External Interference threats
  Stress and strain due to external loads
  Placement of material on or near the pipeline system
  Vibration
  Vegetation management
  Electrical interference
  Land movement
  Common infrastructure corridors
  Temporary pipelines

## Slide 11
Questions?